## Slide 1: Automated Matching for IC Images -- Preliminary and Refinement
Jiawei Gao
July.29th, 2019

## Slide 2: Work steps
1. reconstruct a 3D model from pictures
2. match with the reference

## Slide 3: Reconstruct 3D model
Structure from motion (SfM)
1. Detect SURF features
2. Match points between the previous and the current image
3. Compute the camera pose
4. Triangulate the initial 3-D world points

## Slide 4: Reconstruct 3D model
The result of the reconstruction is very rough and not fine enough.

## Slide 5: Reconstruct 3D model
Two problems:
1. Not enough SURF points in different images
2. Too many useless points

## Slide 6: Calculate norm map of scanned images
Manual coarse alignment:
1. Calculate the rotate angle by hand and rotate back to right position.
2. Crop out one chip in 4 scan directions.
3. Calculate the norm map.

## Slide 7: Result of Norm map’s text region
Upside down "Samsung"

## Slide 8: The autocorrelation of Norm map X
There are periodicities along the x direction.
Offset by one pixel, the autocorrelation coefficient drops significantly

## Slide 9: The height map provided by confocal microscope
The pixels of the microscope are about ten times smaller than the scanner.

## Slide 10: 2D FFT of chip1 in 4 directions
The periodicity can still be observed in the x direction.

## Slide 11: Calculate norm map of scanned images
More accurate preliminary alignment
The function imregcorr in Matlab
Reddy, B. S. and Chatterji, B. N., An FFT-Based Technique for Translation, Rotation, and Scale-Invariant Image Registration, IEEE Transactions on Image Processing, Vol. 5, No. 8, August 1996

## Slide 12: imregcorr
Original image
Translated, rotated and scaled image

## Slide 13: imregcorr
1. Translation
2. Translation and rotation
3. Translation, rotation and scaling

## Slide 14: Translation
Cross-power spectrum

## Slide 15: Translation and rotation
in polar representation

## Slide 16: Scaling
Scale change:
Converting the axes to logarithmic(log) scale, scaling can be reduced to a translational movement(ignoring the multiplication factor 1/(ab) ), i.e.

## Slide 17: Scaling
If is scaled to , the polar representation will be

## Slide 18: Scaling
If is translated, rotated, and scaled replica of , their Fourier magnitude spectra in polar representation are related by

## Slide 19: Overview of the registration algorithm

## Slide 20: Calculate norm map of scanned images
Use one chip’s image to align all images, calculate the ideal template for each chip separately.

## Slide 21: Calculate norm map of scanned images
Correlation for Norm map X
The results show that the correlation of different chips is lower than the correlation of the same chip, no matter background or text regions.

## Slide 22: Thank you